## Slide 1: A631-8 APIM Proposal
Mike Matyas
November 2016
Export of this technology is controlled under the United States Export Administration Regulations (EAR) (15 CFR 300-774). No Export License is required for the dissemination of the commercial information contained herein to non-US persons other than those from or in US government imposed embargoed / sanctioned countries identified in the Supplement 1 to Part 740 (Country Group E) of the EAR. However, an export license is required when dissemination to non-US persons from or in those embargoed / sanctioned countries. It is the responsibility of the individual in control of this data to abide by the U.S. export laws. Export Control Classification Number (ECCN): 7E994.

## Slide 2: A631-8 APIM Proposal
A631-7
  On path toward adoption at 2017 AEEC General Session
  Given implemented ATN B1 CPDLC situation in Europe, A631-7 schedule and scope should not be expanded
A631-8 APIM proposal
  Includes two sets of changes:
    VDL Mode 2 air-ground interoperability tests
    Implementation provisions for connectionless VDL Mode 2
  These changes are intended to further improve VDL Mode 2 operation beyond those made with A631-7

## Slide 3: Air-Ground Interoperability Tests
Experience in Europe has shown that VDL Mode 2 air-ground interoperability tests are desirable
Such tests will:
  Provide greater assurance that VDL Mode 2 will work as intended
  Allow early detection of potential interoperability issues

## Slide 4: Connectionless VDL Mode 2 (1/3)
What
  Allow airplanes and ground stations to exchange messages without having to establish an explicit connection
    Similar to POA (VDL Mode 0/A)
  Exercise previously unused connectionless message exchange capability already described in relevant standards
    ISO 4335/7809, ICAO Doc 9776 (“VDL Tech Manual”) define Unnumbered Information (UI) frame
  Fully compatible with existing VDL Mode 2
    Both variants will work on same frequency at same time
    Airplane could potentially use both variants at same time

## Slide 5: Connectionless VDL Mode 2 (2/3)
Why
  Existing VDL Mode 2 requires airplane and ground station to establish explicit connection
    Less efficient because of resulting overhead message traffic for link establishment, ground station handoff, etc.
    Less robust because airplane accepts uplinks only from connected ground station and only connected ground station accepts downlinks from airplane
  Connectionless VDL Mode 2 is intended to further improve VDL Mode 2 performance
    Airplane will accept uplinks from any ground station and all ground stations will accept downlinks from airplane
    Connectionless data exchange will make ELSA “peer loss of communication” (a.k.a., “N2 events”) less likely to occur

## Slide 6: Connectionless VDL Mode 2 (3/3)
Why (continued)
  Greater efficiency of connectionless VDL Mode 2 will increase effective capacity and accordingly sustainability
    VDL Mode 2 capacity limits are valid concern in Europe and US
  Connectionless VDL Mode 2 will leverage investments already made in VDL Mode 2
    As opposed to starting over with new technology
  Connectionless VDL Mode 2 will be beneficial for IPS
    Boeing, Honeywell, and SITA have performed lab and flight tests of IPS-over-connectionless VDL Mode 2 with positive results

## Slide 7: A631-8 APIM Proposal
Conclusion
  A631-8 APIM proposal includes two sets of changes:
    VDL Mode 2 air-ground interoperability tests
    Implementation provisions for connectionless VDL Mode 2
  These changes are intended to further improve VDL Mode 2 operation
  Please support the proposal