## Slide 1: Ground Companion Comments - 8208 exchanges / GSIF dynamic change
Luc Emberger
July 2020

## Slide 2
GSIF change management (section 2.1.6)
Current text:
“ … each individual ground station must be considered by the aircraft only as an independent access point to a ground network of AOA and/or ATN services and that the specific content of the GSIF from one ground station is not an indication of the overall network status.…
“…It is admitted that the standards are open to various avionics implementation in the case that the ATN service is removed from the current ground station. Different behaviors are existing in real operation. All avionics are initiating a handoff to another ground station but some avionics are initiating an ATN handoff (and then maintain the IDRP adjacency) while others are not.
“… For new avionics implementations, it is recommended to maintain, when possible, the IDRP adjacency in such a case.
Airbus comment:
In case of dynamic change of the GSIF (i.e. loss or gain of ATN capability), only the expected air and ground behavior for ATN connectivity (IDRP) is described. It could be very useful to also describe the consequences on the 8208 connection, and in particular if it shall be considered as maintained or not in these scenarios. Different ground and air assumptions may conduct to a de-synchronisation and unexpected 8208 exchanges.

## Slide 3
GSIF change management (section 2.1.6) – Expected 8208 exchanges
Status of 8208 connection if the GSIF does not advertise ATN anymore:
Shall we consider that 8208 connection is linked to the specific ground station or not impacted by a change of ground station ?
Should the airborne system consider that 8208 connection is broken (even without receiving a Clear Request)? Some avionics will consider that ATN is down and automatically clear the 8208 connection (with or without sending an 8208 Clear Request to the ground, in particular if the connection is considered already closed).
Proposal 1:
Clarify that all 8208 connections established via a ground station are considered closed when this ground station does not advertise ATN anymore (TBC)
Note: An alternative not detailed in this presentation would be to consider that 8208 connection is maintained if no 8208 Clear Request is received from the ground

## Slide 4
GSIF change management (section 2.1.6) – Expected 8208 exchanges
Expected 8208 exchanges when the airborne recovers ATN via a new ground station (with or without maintaining IDRP after the GSIF does not advertise ATN anymore):
As per ARINC 631, the airborne system should send a new 8208 Call Req in the CMD-LE or CMD- HO when trying to establish a new ATN connection via a new ground station:
« 9.4.1 … An aircraft crossing, within the same Ground System, two Ground Stations connected to the same VSDA (whether the ground system supports X.121 addressing or not), should send a handoff (XID_CMD_HO) to the new ground station. In this case, an ISH PDU should also be included in the Call Request even though route initiation and exchange of configuration information should not occur.”
“ 9.4.1.1 New Call per Hand-Off
Every time a handoff is to be implemented, the Call_request packet should be
generated from the aircraft to the VGS and the ground should respond with a
Call_confirm packet.”
Proposal 2:
- Clarify that a new 8208 connection will be established by the airborne system via a different eligible ground station (if available in the PECT), whatever the IDRP status is (maintained or not).

## Slide 5
GSIF change management (section 2.1.6) – Expected 8208 exchanges
Expected 8208 exchanges, if no other ATN capable VGS is available in the PECT, and an AOA link is maintained with the VGS:
It may happen that no other VGS in the PECT advertises ATN. In that case, the airborne system may remain connected on the current VGS, to maintain the AOA link. If ATN capability comes back in the GSIF, is it needed to establish a new 8208 connection (no CMD-LE, nor CMD-HO is exchanged in this situation)?
Proposal 3 (if proposal 1 is agreed):
Clarify that when ATN becomes available via a ground station an airborne system is already connected with, in AOA mode, a new 8208 connection will be established by the airborne system
Note: it is considered that if no other VGS is ATN capable and eligible in the PECT, in any case IDRP cannot be maintained

## Slide 6
Thank you
© Airbus S.A.S. All rights reserved. Confidential and proprietary document. This document and all information contained herein is the sole property of AIRBUS. No intellectual property rights are granted by the delivery of this document or the disclosure of its content. This document shall not be reproduced or disclosed to a third party without the express written consent of AIRBUS S.A.S. This document and its content shall not be used for any purpose other than that for which it is supplied. The statements made herein do not constitute an offer. They are based on the mentioned assumptions and are expressed in good faith. Where the supporting grounds for these statements are not shown, AIRBUS S.A.S. will be pleased to explain the basis thereof. AIRBUS, its logo, A300, A310, A318, A319, A320, A321, A330, A340, A350, A380, A400M are registered trademarks.