## Slide 1: Common IPS radio interface Proposal for adoption in A858 - sup. 1
Michal Skořepa
Zdeněk Jaroň
AEEC IPS
August 04, 2021

## Slide 2: Common IPS radio interface - Reminder
Motivation
  Airborne Radio-specific interfaces  diverse environment  not all radios provide the same information/capabilities to the Aiborne IPS System
    Main concerns: datalink status signaling, flow control
Recommendation
  Define a common control-plane format and protocol for all airborne radios
    Support IPS needs
    Plug&Play style
    Extended set of link status information (e.g. „degraded“, or fine-grained link quality)
    Flow control support
    Extensible and future-proof
  Define a common way of handling data plane for all radios
    QoS-related aspects (e.g. differentiating among data packets with different criticalities)
    Multilink-related aspects (e.g. provisions for signalling of problems delivering some packets  re-routing to a different link)

## Slide 3: Common IPS radio interface: Prioritization
Prioritization and flow control support require:
    The control plane interface to support exchanging flow control information between Airborne IPS System and Airborne Radios
    The data plane interface to provision differentiation among data packets of different priorities/QoS  multiple approaches may be taken
      Separate logical interfaces for high priority data and low priority data in Airborne IPS System
      DSCP tagging utilization
      Meta-data on the data plane interface
Additional consideration – PP858 commentary:
    „In accordance with ICAO Annex 10, Volume III, distress and urgent communications are prioritized over ATS and AOC safety and regularity of flight communications.“

## Slide 4: addressing prioritization
Airborne IPS System
Radio
interface
Radio *
L1
“L2”
Multilink decision
Routing
IPS Prio 1
IPS Prio 2
Prio2
Scheduler
Prio1
Prio2a
Prioritization
The Airborne IPS system has two logical interfaces to the radio – one for high priority data such as CPDLC and ADS-C (“Prio1”) and one for low priority data such as typical AOC (“Prio2”). (This can be extensible to more interfaces if needed.) The basic prioritization within the Airborne IPS system means simply sending the data to the right interface.
Prio2b
Prio1
Each logical interface can be throttled, based on the amount of data queued within the corresponding queue in the radio. This may be used to further prioritize among the different types of high or low priority data (e.g. “Prio2a”, “Prio2b”) within the Airborne IPS system.
Flow control
The radio queue status information is also used as a complementary input to the multilink decision engine (e.g. may be translated to a specific “congested” status information). This link decision and the rerouting is done independently for different priorities of data and the results are signaled to the ground via AGMI.
The radio L2 scheduler ensures (through strict prioritization or other link-specific mechanism) that the Prio1 data can meet the applicable performance requirements in the presence of arbitrary amount of Prio 2 data. This is the only place where truly strict prioritization in the aircraft can happen! (Because there is no further queueing below.)
AISD
AISD
* For VDLm2 the term Radio represents both the VDR part and the CMU part.

## Slide 5: Proposal – Atn/IPS Aircraft Protocol (AIAP)
Protocol operation
    Airborne IPS System periodicaly polls the Airborne Radio for status
      Airborne Radio responds with its status
      If the Airborne radio does not respond after a configurable no. of retries, it is treated as non-functional
Message format
    TLVs (Type-Lentgth-Value) with multiple Options
Independent of underlying on-board network
    Prototyped and validated on Ethernet with UDP/IPv4 stack
    Well suited for AFDX networks
    May require further considerations for A429
Proof-of-concept solution developed by Honeywell to address the needs of link status signaling and flow control

## Slide 6: AIAP – conveyed information
control-plane AIAP options
    Datalink ID – identifies the radio/datalink in scope of the aircraft
    Datalink Status – basic discrete datalink status (e.g., UP, DOWN, DEGRADED)
    Link Instance – identifies the current CSP
    Datalink Context – indicates need to repeat a multilink signaling interface message
    Queue Status – status of a queue for a CoS
    Packet State – indicates state of a packet with given Packet ID
data-plane AIAP options
    Packet Data – carries the packet itself
    Packet CoS – identifies class of service of the packet
    Time to Live – maximum time of packet usefulness
    Packet ID – unique identifier for the packet
from radio* to Airborne IPS system
from Airborne IPS system to radio*

## Slide 7: AIAP Control-plane MSC

## Slide 8: AIAP control-plane message structure

## Slide 9: AIAP Data-plane MSC

## Slide 10: AIAP Data-plane message structure

## Slide 11: Next Steps
Agree on the technical solution
    Start with Honeywell AIAP solution, which has been prototyped and validated in representative environments
    Draft A858 Supplement 1 text based on the AIAP specification, and refinements by the AEEC IPS Subcommittee
Update Radio Standards
    Update radio standards to reference the interface specification in A858-sup1
      ARINC 781 (Inmarsat), ARINC 771 (Iridium), ARINC 758 (CMU)? (implementation specific?)
    Radio standards update schedule
      TBD

## Slide 12: Backup

## Slide 13: Motivation for flow control - prioritization PP858: section 3.3.5
ATS shall be prioritized over AOC data
  ATS is subject to stringent RCP/RSP monitoring and inability to pre-empt queued AOC data would imply that we’d have to meet the RCP and RSP also for all AOC data.
  Already today we have more AOC traffic than ATS and this disproportion will likely grow.
Prioritization shall be applied among AOC data
  There are very different types of “AOC” applications (weather vs. maintenance vs. flight planning…) and we want to allow users and developers to decide which is more time-critical.
    Do we want to fully download 1MB of maintenance data before we dispatch a request for flight plan update?
Prioritization shall be applied among ATS data
  Some ATS application data may be more critical than others – mainly for future ATS services
    Existing ATS applications (CPDLC, ADS-C) produce just sporadic and irregular messages, all subject to RCP/RSP. So currently there is not much to queue and prioritize

## Slide 14: Baseline queueing architecture
Radio
L1
“L2”
Airborne IPS System
Multilink decision
Routing
ATS app
AOC app
Radio Queue
IPS Queue
IPS router sees the radio as a single logical interface  there is a single output queue, throttled only by the throughput of the physical interface towards the radio.
Scheduler
AOC msg
AOC msg
AOC msg
ATS msg
AOC msg
AOC msg
Real bottleneck is the radio’s physical layer (L1). The L2 scheduler dispatches message from the radio queue only when there is L1 resource available (time slot in TDMA system).
Radio doesn’t implement any prioritization  there is common transmit queue for all types of messages  any ATS message needs to wait until all previously queued AOC messages are dispatched.
IMPORTANT: Radio L1 will always be the bottleneck and there will always be some queues in the radio.
Not good
Radio
interface
AOC msg
AOC msg
UPDATE?

## Slide 15: Static throttling in airborne IPS system
Radio
L1
“L2”
Airborne IPS System
Multilink decision
Routing
ATS app
AOC app
Radio Queue
We can statically throttle the output towards the radio based on some expected a/g throughput. But this doesn’t really solve the problem! The a/g throughput is variable. If we throttle to minimum a/g throughput we’d be using the link extremely inefficiently most of the time. If we throttle to anything higher, data can still queue in the radios.
Scheduler
ATS Queue
AOC Queue
Prioritization
We can implement prioritization in the airborne IPS system with separate ATS and AOC queues, only if we throttle the output towards the radio. (The “Prioritization” function always checks the ATS message queue first.)
Not helpful
Radio
interface
AOC msg
AOC msg
AOC msg
ATS msg
AOC msg
AOC msg
AOC msg
AOC msg
IMPORTANT: This is the only option for some radios, that do not provide any congestion information.
UPDATE?

## Slide 16: throttling based on SDU queue status
Airborne IPS System
Radio
interface
Radio
L1
“L2”
Multilink decision
Routing
ATS app
AOC app
Radio Queue
Instead of static throttling we throttle based on the status of the common radio queue. Thus we can reduce the ammount of data queued in the radio to some “watermark level” and thereby reduce the worst/case dispatch time for an ATS message.
Scheduler
AOC msg
AOC msg
ATS msg
AOC msg
ATS Queue
AOC Queue
Prioritization
Partially helpful
Flow control (e.g. queue status)
But we can’t reduce the size of this queue too much, because:
The amount of queued data may drive the amount of resources (time slots) allocated to the terminal by the network (in case of e.g. Satcom) – the more data is queued, the more resources we request.
The radios typically have their own retransmission mechanisms and data are removed from the queue only once ack’d from ground. Reducing the queue size to 1 would be an ACARS like “send-and-wait” solution with very poor throughput.
IMPORTANT: If we want to go this way, we’d have to prove for certification one of the following:
We can meet the RCP/RSP even when the queue is always full, when ATS message arrives (…which significantly increases the demanded a2g link performance)
AOC applications get queued in the radio only sparsely (…which can’t be proven)
UPDATE?