## Slide 1: Method to increase the number of arinc 718 program pins
March, 2020
AEEC Traffic Surveillance
Douglas Guetter, ACSS Systems Engineer

## Slide 2: Program Pin Strobing concept introduced in ARINC 718A
Strobing was introduced in order to increase the number of program pin settings
Basic concept:
    Program pins can be specified as “Open”, “Ground”, or “Strobed” thus giving three states for each program pin.
    An existing output discrete (XPDR Fail Discrete #1) was defined as the strobe.
    On power-up, the strobe is toggled and the software determines whether the program pin is “Open”, “Ground”, or connected to the “Strobe”.
Output discrete
Program Pin
Output discrete
Program Pin
Common
Common
Output discrete
Program Pin
Common
Strobed, State = 2
Grounded, State = 1
Open, State = 0

## Slide 3: Expansion of the Strobing concept
If additional “strobe” Program outputs are defined, the input discrete pin states can be expanded.
With 6 Program output discretes, 8 states are possible for each input discrete.
    The first Program output pin is toggled and each of the strobed discretes (inputs) are read.
    The next Program output is toggled and each of the strobed discretes are read.
    Continue the same process for all of the Program outputs until all the Program outputs have been toggled once.
    Assign the state to each strobed discrete. An example state table for 6 Program outputs is shown on the next slide.

## Slide 4: Expansion of the Strobing concept
Condition | State
Open: if a program pin is “open” when read | 0
Ground: if a program pin is connected to ground/common when read | 1
Strobe 1: f a program pin is connected to “Program Output discrete #1” when read | 2
Strobe 2: f a program pin is connected to “Program Output discrete #2” when read | 3
Strobe 3: f a program pin is connected to “Program Output discrete #3” when read | 4
Strobe 4: f a program pin is connected to “Program Output discrete #4” when read | 5
Strobe 5: f a program pin is connected to “Program Output discrete #5” when read | 6
Strobe 6: f a program pin is connected to “Program Output discrete #6” when read | 7