## Slide 1: Aircraft Type Program Pin Options Analysis Stephen Darr, Dynamic Aerospace Inc 10 December 2020
ARINC Airline Electronic Engineering Committee (AEEC) Traffic and Weather Surveillance Subcommittee

## Slide 2: DO-260C ADS-B Aircraft State Message Requirements- Aircraft Type
2.2.3.2.7.6.3.3 “Aircraft Type” Subfield in ADS‑B Wx Aircraft State Messages
The “Aircraft Type” subfield is a 24-bit (“ME” bits 12 – 35, Message bits 44 – 67) field that is used to report the aircraft ICAO Type Designator for the Manufacturer and Model aircraft, per ICAO Doc 8643. Aircraft Type may be configured during ADS‑B system installation.
The character in each of the “Aircraft Type Char #” subfields is encoded as a 6-bit subset of the International Alphabet Number 5 (IA-5) in accordance with Appendix A, §A.1.4.4.1 Table A-5 of these MOPS.
Note: International Alphabet No. 5 (IA-5) is defined in full in ICAO, Annex 10, Volume III, Part 1, Table 8-2.
If Aircraft Type is not available to the ADS‑B Transmitting Subsystem, then each of the “Aircraft Type Char #” subfields shall be set to ALL ZEROs (binary 000000).

## Slide 3: “Wasted Space” in 6-Bit Character Encoding
“ADS‑B Wx AIREP Message (Aircraft State) (TYPE=26, Subtype=0)”
Table A-5: Aircraft Identification Character Coding
Msg Bit # | 44 – 49 | 50 – 55 | 56 – 61 | 62 – 67
“ME” Bit # | 12 – 17 | 18 – 23 | 24 – 29 | 30 – 35
Field Name | Aircraft Type Char #1 | Aircraft Type Char #2 | Aircraft Type Char #3 | Aircraft Type Char #4
Bits | 6 | 6 | 6 | 6
 | MSB | MSB | MSB | MSB
 | LSB | LSB | LSB | LSB
Only 37 of 64 possible values are used to encode the IA-5 6-bit subset |  |  |  | 
1SP = SPACE code |  |  |  | b6 | 0 | 0 | 1 | 1
 |  |  |  | b5 | 0 | 1 | 0 | 1
b4 | b3 | b2 | b1 |  |  |  |  | 
0 | 0 | 0 | 0 |  |  | P | SP1 | 0
0 | 0 | 0 | 1 |  | A | Q |  | 1
0 | 0 | 1 | 0 |  | B | R |  | 2
0 | 0 | 1 | 1 |  | C | S |  | 3
0 | 1 | 0 | 0 |  | D | T |  | 4
0 | 1 | 0 | 1 |  | E | U |  | 5
0 | 1 | 1 | 0 |  | F | V |  | 6
0 | 1 | 1 | 1 |  | G | W |  | 7
1 | 0 | 0 | 0 |  | H | X |  | 8
1 | 0 | 0 | 1 |  | I | Y |  | 9
1 | 0 | 1 | 0 |  | J | Z |  | 
1 | 0 | 1 | 1 |  | K |  |  | 
1 | 1 | 0 | 0 |  | L |  |  | 
1 | 1 | 0 | 1 |  | M |  |  | 
1 | 1 | 1 | 0 |  | N |  |  | 
1 | 1 | 1 | 1 |  | O |  |  | 

## Slide 4: “Wasted Space” in Type Designator Encoding
Type Designator Character Assignment
Character 1
  Alpha characters only
    26 possible values (A-Z)
    0-9 not allowed
    ‘Space’ not allowed
Characters 2-4
  Alpha-numeric values
    37 possible values
      A-Z (26), 0-9 (10), ‘Space’ (1)
No intervening ‘Space’ characters
Valid Aircraft Type Designators
Count | Char 1 | Char 2 | Char 3 | Char 4
26 | Alpha | Space | Space | Space
936 | Alpha | Alpha-numeric | Space | Space
33,696 | Alpha | Alpha-numeric | Alpha-numeric | Space
1,213,056 | Alpha | Alpha-numeric | Alpha-numeric | Alpha-numeric
= 1,247,714 | Total valid Aircraft Type Designators |  |  | 

## Slide 5: Save Space and Pins?
With 6 Strobe Pins…
One Program Pin provides for eight unique values (23 or 3-bits)
  Two pins provides for 23x2 = 26 or 64 unique values (6-bits)
Seven Program Pins provides for 23x7 = 221 or 2,097,152 unique input values (21-bits)
Eight Program Pins provides for 23x8 = 224 or 16,777,216 unique input values (24-bits)
What’s Required
1,247,714 valid Type Designators
  Only 10,245 aircraft were assigned a Type Designator as of 08 December 2020 (fewer unique values exist as many aircraft share duplicate values)
21-bit, 7-pin input
  1,247,714 / 2,097,152 = 59.5% max fill ratio for valid values
24-bit, 8-pin input
  1,247,714 / 16,777,216 = 7.4% max fill ratio for valid values

## Slide 6: 7 Program Pin Encoding
Valid Type Designators are ‘Packed’
Packing sequentially orders valid Aircraft Type Designator so that no intervening invalid values exist
Intervening space characters are not allowed; therefore, the valid values are grouped in 3 ranges associated with trailing spaces and one range without any spaces, as shown on chart 4
Installation Considerations
Aircraft Type Designator to binary number mapping must be specified (example ranges shown on chart 4 are used for decode logic example on chart 7)
Installation guidance for wiring of 7 program pins is needed to ensure correct 21-bit binary value

## Slide 7: 7 Program Pin Decoding Logic Example
Character Value Lookup Table
Character | Char Value | Character | Char Value
A | 0 | S | 18
B | 1 | T | 19
C | 2 | U | 20
D | 3 | V | 21
E | 4 | W | 22
F | 5 | X | 23
G | 6 | Y | 24
H | 7 | Z | 25
I | 8 | 0 | 26
J | 9 | 1 | 27
K | 10 | 2 | 28
L | 11 | 3 | 29
M | 12 | 4 | 30
N | 13 | 5 | 31
O | 14 | 6 | 32
P | 15 | 7 | 33
Q | 16 | 8 | 34
R | 17 | 9 | 35
Character Decode Logic
‘N’ is decimal value (0-2,097,152) associated with 7-pin binary number
‘N’ in range 0-25
  Char 1 = Lookup(N)
  Char 2 = Char 3 = Char 4 = Space
‘N’ in range 26-961
  Char 1 = Lookup(Truncate((N-26)/36))
  Char 2 = Lookup((N-26)-Char 1 Val*36))
  Char 3 = Char 4 = Space
‘N’ in range 962-34,657
  Char 1 = Lookup(Truncate((N-962)/1236))
  Char 2 = Lookup(Truncate(((N-962)-(Char 1 Val*1236))/36))
  Char 3 = Lookup((N-962)-(Char 1 Val*1236)-(Char 2 Val*36))
  Char 4 = Space
‘N’ in range 34,658-1,247,713 (‘N’ > 1,247,713 is invalid)
  Char 1 = Lookup(Truncate((N-34,658)/46,656))
  Char 2 = Lookup(Truncate(((N-34,658)-(Char 1 Val*46,656))/1236))
  Char 3 = Lookup(Truncate(((N-34,658)-(Char 1 Val*46,656)-(Char 2 Val*1236))/36))
  Char 4 = Lookup((N-26)-(Char 1 Val*46,656)-(Char 2 Val*1236)-(Char 3 Val*36))

## Slide 8: 8 Program Pin Encoding
Type Designator Character Programming
Each Aircraft Type Designator character is specified by a 2-pin pair
  Four, 2-pin pairs = 8 pins
Installation Considerations
Character to binary number mapping must be specified, e.g. as for IA-5
Installation guidance for wiring of four, 2-pin pairs is needed to ensure correct 6-bit binary value is associated with each character

## Slide 9: 8 Program Pin Decoding Logic
IA-5 6-bit Subset Character Value Lookup Table
Character Decode Logic
‘Nx’ is one of four decimal values associated with each of four, 2-pin pair binary numbers
  Unique (decimal) values = 0-63
  Valid (decimal) values = 1-26, 32, and 48-57
Char 1 = Lookup(N1)
  Valid values limited to (decimal) 1-26
Char 2 = Lookup(N2)
Char 3 = Lookup(N3)
Char 4 = Lookup(N4)
Apply logic to ensure no intervening spaces exist
1SP = SPACE code |  |  |  | b6 | 0 | 0 | 1 | 1
 |  |  |  | b5 | 0 | 1 | 0 | 1
b4 | b3 | b2 | b1 |  |  |  |  | 
0 | 0 | 0 | 0 |  |  | P | SP1 | 0
0 | 0 | 0 | 1 |  | A | Q |  | 1
0 | 0 | 1 | 0 |  | B | R |  | 2
0 | 0 | 1 | 1 |  | C | S |  | 3
0 | 1 | 0 | 0 |  | D | T |  | 4
0 | 1 | 0 | 1 |  | E | U |  | 5
0 | 1 | 1 | 0 |  | F | V |  | 6
0 | 1 | 1 | 1 |  | G | W |  | 7
1 | 0 | 0 | 0 |  | H | X |  | 8
1 | 0 | 0 | 1 |  | I | Y |  | 9
1 | 0 | 1 | 0 |  | J | Z |  | 
1 | 0 | 1 | 1 |  | K |  |  | 
1 | 1 | 0 | 0 |  | L |  |  | 
1 | 1 | 0 | 1 |  | M |  |  | 
1 | 1 | 1 | 0 |  | N |  |  | 
1 | 1 | 1 | 1 |  | O |  |  | 

## Slide 10: Decision: 7-Pin vs. 8-Pin?
Does the value of being able to reserve a single pin for future use outweigh the complication associated with the 7-pin approach vs. the 4 x 2-pin (8-pin) approach?

## Slide 11: Questions
Stephen Darr
sdarr@dynamicaerospace.com
+1 (339) 364-0955